## Slide 1: RISC-V & HPC
Guided by :
Mr. Surendra Billa Sir
Mr. Rushikesh Jadhav Sir
Project P5:
Mr. Tejas Bhanudas Katkar PRN-230940130035
Mr. Bhanu Prakash Agrawal PRN-230940130015
Ms. Muskan Sharma PRN-230940130037
Ms. Akanksha Abhay Ghorpade PRN-230940130025

## Slide 2: Instruction Set Architecture
Software
Hardware

## Slide 3: Why RISC-V ?

## Slide 4: ARM vs RISC V : ISA Comparison
ISAs can be broadly categorized into two types:
1→Open ISA
2→Closed ISA
Closed ISAs, like ARM, are proprietary and tightly controlled by specific companies (Arm Holdings here), offering established reliability and compatibility but limiting customization.
Open ISAs, exemplified by RISC-V, are community-driven and provide greater flexibility for customization, fostering innovation and adaptation to specific needs.

## Slide 5
3 main advantages of RISC-V
Flexibility
Control
Visibility

## Slide 6
Risc-V Architecture

## Slide 7: Cross Compiler Toolchain (Flow)

## Slide 8: Vector Processing in HPC

## Slide 10: THEJAS32 SoC
THEJAS32 SoC is based on the VEGA ET1031 processor, which is a 32 bit single core in-order, 3-stage pipeline processor. This processor is based on the open source RISC-V Instruction Set Architecture and operates at a frequency of 100MHz. The SoC also includes peripherals like 256KB internal SRAM, Three UARTs, Four SPIs, Three TIMERs, Eight PWMs, Three I2C interfaces, 32 GPIOs etc. This SoC is designed and developed by Centre for Development of Advanced Computing (C-DAC) as part of the Digital India RISC-V (DIR-V) Program, by the Ministry of Electronics and Information Technology, Government of India.

## Slide 11: SIMD : Single instruction Multiple Data
How SIMD Operates ?

## Slide 12: Vector Processing
Vector Processing Architecture
  Memory to Memory Architecture (Traditional)
  Register to Register Architecture (Modern)
Components of vector processors
  Vector Registers
  Vector functional Units
  Vector load-store Units
  Scalar Registers
Advantages of Vector processing
  Quick fetch and decode of single instruction for multiple operations
  Easier Addressing of main memory
  Elimination of memory Wastage
  Simplification of control hazards
  Reduced code size

## Slide 14: RISC-V V/S RISC-V V
Risc-v
–Base instruction Set Architecture
–Focuses in Scalar Operations
–Handles individually data elements
–Performance is less as compared to RVV
–Easy to understand
–Widely Adopted
Risc-v v
–Optional extension adds capabilities of SIMD
–Focuses on Vector Operations
–Handles multiple data elements
–Designed to work on large data sets
–High Performance
–RVV support is growing but not universally implemented on all all Risc-v

## Slide 15
RISC-V VECTOR EXTENSION
Unleashing Parallelism in RISC-V Architecture

## Slide 16: RISC-V EXTENSIONS

## Slide 17: INTRODUCTION
What it is: A set of instructions for RISC-V processors that enable them to perform vector operations.
What it does: Allows processing multiple data elements at once, leading to faster performance for specific tasks.
When it's useful: For tasks involving large amounts of data and repetitive calculations, such as:
  Signal processing
  Image and video processing
  Machine learning
  Scientific computing

## Slide 18: OVERVIEW OF ITS FEATURES AND CAPABILITIES
SIMD (Single Instruction, Multiple Data): Allows a single instruction to perform the same operation on multiple data elements simultaneously, exploiting data-level parallelism.
Enhanced Performance: By processing multiple data elements in parallel, the Vector Extension significantly improves throughput and efficiency for tasks such as multimedia processing, scientific computing, and machine learning.
Customizable Vector Length: Supports vectors of variable lengths, enabling optimization for different applications and target platforms.
Vector Registers: Dedicated vector registers hold vector data, facilitating efficient manipulation and computation.
Vector Memory Accesses: Supports efficient vector memory accesses, reducing overhead in loading and storing vector data.
Predication Support: Enables conditional execution based on vector elements, enhancing flexibility in control flow.

## Slide 19: RISC-V RV64GV TOOLCHAIN

## Slide 20: RISC-V VECTOR INSTRUCTION

## Slide 21: RISC-V SCALAR INSTRUCTION

## Slide 22: RISC-V MAKEFILE INSTRUCTION

## Slide 23: EXPLORING RISC-V VECTOR EXTENSION WITH QEMU

## Slide 24: X_86 ARCHITECTURE
Scalar Instruction
Vector Instruction

## Slide 25: EXPLORING VECTOR EXTENSION WITH X_86 ARCHITECTURE

## Slide 26: CHALLENGES AND LIMITATIONS
Programming Complexity: Utilizing vector instructions effectively requires specialized programming techniques such as loop unrolling, data alignment, and explicit vectorization, which can increase code complexity and development time.
Data Dependency: Dependencies among vector elements can limit parallelism and lead to inefficient utilization of vector resources, especially in algorithms with irregular data access patterns or conditional branching.
Memory Bandwidth: Vectorized operations can impose significant demands on memory bandwidth, especially for large vector lengths, leading to potential bottlenecks and inefficiencies in memory-bound applications.
Hardware Complexity: Implementing a high-performance vector unit entails additional hardware resources and complexity, including wider data paths, vector registers, and efficient memory access mechanisms, which may increase design complexity and power consumption.
Software Ecosystem: The availability of software tools, libraries, and compilers optimized for the Vector Extension may be limited compared to established architectures, posing challenges for developers in leveraging its full potential.

## Slide 27: AREAS FOR IMPROVEMENT AND ONGOING RESEARCH
Compiler Optimization: Continued research is needed to develop advanced compiler techniques for automatic vectorization, loop restructuring, and optimization of memory access patterns to extract maximum parallelism from applications.
Vectorization Libraries: Further development of vectorization libraries and frameworks tailored for the Vector Extension can simplify programming and accelerate adoption by providing high-level abstractions and optimized routines for common tasks.
Memory Hierarchy: Research into efficient data prefetching, caching strategies, and memory hierarchy designs is crucial to mitigate the impact of memory bandwidth limitations and improve overall system performance.
Scalability and Heterogeneity: Investigating techniques for scalable vector processing across multiple cores and heterogeneous architectures, including integration with multi-core processors and accelerators, can enhance performance and flexibility in diverse computing environments.
Energy Efficiency: Optimizing vector architectures for energy efficiency through techniques such as dynamic voltage and frequency scaling, power gating, and instruction-level energy reduction is essential for enabling high-performance, energy-efficient computing systems.

## Slide 28: DIY LINUX – What?

## Slide 29: DIY LINUX – Why?

## Slide 30: DIY LINUX – Where? – RVV (RISC-V Vector)
riscv64-gv (RV64GV)

## Slide 31: DIY LINUX – How?
Configuring the Environment
Making cross Toolchain

## Slide 32: DIY LINUX – How?
Configuring the Environment

## Slide 33: DIY LINUX – How?
Configuring the Environment
  bin

## Slide 34: DIY LINUX – How?
Configuring the Environment
  usr

## Slide 35: DIY LINUX – How?
Configuring the Environment
  var

## Slide 36: DIY LINUX – How? – Toolchain

## Slide 37: DIY LINUX – How? –
Toolchain

## Slide 38: DIY LINUX – How? –
Kernel Headers - includes

## Slide 39: DIY LINUX – How? –
Kernel Headers – architecture dependent

## Slide 40: DIY LINUX – How? –
Kernel Headers - drivers

## Slide 41: DIY LINUX – How? –
Kernel Headers – file system

## Slide 42: DIY LINUX – How?
Compiler

## Slide 43: DIY LINUX – How?
Compiler –Resources to build compiler

## Slide 44: DIY LINUX – How?
Cross-Compiler

## Slide 45: DIY LINUX – How?
Cross-Compiler - build

## Slide 46: DIY LINUX – How?
Cross-Compiler - contains

## Slide 47: DIY LINUX – How?
Cross-Compiler executable test

## Slide 48: DIY LINUX – How?
Cross-Compiler - Application

## Slide 49
THANK YOU !